## Slide 1
Campus Network Design and Packet Trace Simulator
Computer Networks Laboratory CSE20110
15 seconds
Campus Packet Lab
Computer Networks Laboratory (CSE20110)
Department of Computer Engineering and Technology
Ajinkya Katke – 1262243726 Tattwam Samui – 1262242400
Akshat Pandey – 1262242316 Smith Hajgude – 1262242364
Shlok Pandey – 1262243751
Panel J Batch J2
Faculty: Dr. Uma Pujeri
Academic Year: 2026–2027
GitHub: https://github.com/AsHx-BiT/Campus-Network-
Notes: Introduce the project title and the five team members.

## Slide 2
Problem and Objectives
Computer Networks Laboratory CSE20110
40 seconds
Problem
A campus needs separate networks for administration, teachers, students and library users.
The design should let each group communicate while keeping traffic organized.
Objectives
1. Divide the campus LAN into four VLANs.
2. Route between VLANs with one router trunk.
3. Provide DHCP, DNS and a school web page, then trace sample packets.
Notes: Explain that VLANs separate users by department. The router provides communication between VLANs, and the server provides campus services.

## Slide 3
Proposed Design and Tools
Computer Networks Laboratory CSE20110
45 seconds
Tools: Cisco Packet Tracer; companion dark-theme web simulator
Protocols: 802.1Q trunk, IPv4, DHCP, DNS and HTTP
Server: 192.168.40.10 | Gateway: .1 in each subnet
R1 · 2911
SW1 · 2960
VLAN 10 · ADMIN
A1, A2
192.168.10.0/24
VLAN 20 · TEACHERS
T1, T2
192.168.20.0/24
VLAN 30 · STUDENTS
S1, S2
192.168.30.0/24
VLAN 40 · LIBRARY
L1, L2 · Server
192.168.40.0/24
Notes: Point out the router-on-a-stick link between R1 and SW1. The switch connects two clients in each VLAN and a server in VLAN 40. Each group uses a separate /24 subnet.

## Slide 4
Implementation and Working
Computer Networks Laboratory CSE20110
55 seconds
Implementation: VLAN access ports, router subinterfaces and DHCP pools. Server .10 runs DNS and HTTP.
Working: A VLAN tag reaches R1; R1 routes to the destination VLAN and SW1 forwards the frame.
Fix applied: enable R1 Gi0/0; reserve the server IP from DHCP.
interface GigabitEthernet0/0.10
encapsulation dot1Q 10
ip address 192.168.10.1 255.255.255.0
! Repeat for VLANs 20, 30 and 40
Notes: Explain the VLAN 10 subinterface as an example; the same pattern is used for VLANs 20, 30 and 40. DHCP assigns client addresses. The server has a fixed address. The original router interface was shutdown, so it was enabled to bring up the trunk.

## Slide 5
Testing and Results
Computer Networks Laboratory CSE20110
50 seconds
A1 (VLAN 10) → SW1 → R1 → SW1 → Server (VLAN 40)
TCP destination port 80 | 4 network hops | TTL 64 → 63
Test: simulator model, A1 → Server using TCP port 80.
Expected: cross-VLAN traffic is routed by R1 to the server subnet.
Observed: path includes R1; modeled TTL decreases by one.
Also checked: same-VLAN path bypasses R1; DNS uses server 192.168.40.10.
Notes: These results come from the website packet-trace model and API checks, not a live Packet Tracer runtime test. Explain the modeled route and the cross-VLAN TTL change.

## Slide 6
Working Demonstration
Computer Networks Laboratory CSE20110
65 seconds
Function to demonstrate
Show how a packet moves from a client in one VLAN to the campus server in another VLAN.
1. Open the completed .pkt in Cisco Packet Tracer and show the topology.
2. In the local website, choose A1 → Server, TCP port 80, then run Trace.
3. Compare the route and hop details with the VLAN layout.
Success: the trace crosses R1 between VLANs and reaches the server.
Notes: Prepare Cisco Packet Tracer and start the local website before presenting. In Packet Tracer, show the network layout. In the website, run the A1-to-Server trace and explain that it is the companion simulator’s modeled path.

## Slide 7
Conclusion and Contributions
Computer Networks Laboratory CSE20110
30 seconds
Outcome: four VLANs, DHCP, DNS and a campus web server are configured in the project.
Use: demonstrate department separation and inter-VLAN routing.
Limitation: website traces are modeled; live Packet Tracer traffic was not tested here.
Future: add more campus services and security rules.
Team contribution: Ajinkya Katke, Tattwam Samui, Akshat Pandey, Smith Hajgude and Shlok Pandey — project team.
AI use: helped build the companion simulator and configuration guidance; details checked against the project files.
Notes: Summarize the four-VLAN design and explain that the website is a companion teaching model. Do not present its trace results as live Packet Tracer results.

## Slide 8
References
Computer Networks Laboratory CSE20110
Backup slide
[1] Cisco Networking Academy, “Cisco Packet Tracer,” https://www.netacad.com/catalogs/learn/cisco-packet-tracer.
[2] Cisco, “Configure Inter VLAN Routing with the Use of an External Router,” https://www.cisco.com/c/en/us/support/docs/lan-switching/inter-vlan-routing/14976-50.html.
[3] R. Droms, “Dynamic Host Configuration Protocol,” RFC 2131, IETF, Mar. 1997.
Project evidence: Group_project_completed.pkt and the Campus Packet Lab local website.
Notes: The first two references describe Packet Tracer and router-based inter-VLAN routing. RFC 2131 specifies DHCP.